## Slide 1: Chapter 2. Machine Instructions and Programs

## Slide 2: Objectives
Machine instructions and program execution, including branching and subroutine call and return operations.
Number representation and addition/subtraction in the 2’s-complement system.
Addressing methods for accessing register and memory operands.
Assembly language for representing machine instructions, data, and programs.
Program-controlled Input/Output operations.

## Slide 3: Number, Arithmetic Operations, and Characters

## Slide 8: Signed Integer
3 major representations:
Sign and magnitude
One’s complement
Two’s complement
Assumptions:
4-bit machine word
16 different values can be represented
Roughly half are positive, half are negative

## Slide 10: Sign and Magnitude Representation
High order bit is sign: 0 = positive (or zero), 1 = negative
Three low order bits is the magnitude: 0 (000) thru 7 (111)
Number range for n bits = +/-2n-1 -1
Two representations for 0

## Slide 13: One’s Complement Representation
Subtraction implemented by addition & 1's complement
Still two representations of 0! This causes some problems
Some complexities in addition

## Slide 17: Two’s Complement Representation
Only one representation for 0
One more negative number than positive number
like 1's comp
except shifted
one position
clockwise

## Slide 25: Binary, Signed-Integer Representations
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
0
0
1
1
0
0
0
0
1
1
0
0
1
1
1
0
1
0
1
0
1
0
0
1
0
1
0
1
0
1
1
+
1
-
2
+
3
+
4
+
5
+
6
+
7
+
2
-
3
-
4
-
5
-
6
-
7
-
8
-
0
+
0
-
1
+
2
+
3
+
4
+
5
+
6
+
7
+
0
+
7
-
6
-
5
-
4
-
3
-
2
-
1
-
0
-
1
+
2
+
3
+
4
+
5
+
6
+
7
+
0
+
7
-
6
-
5
-
4
-
3
-
2
-
1
-
b
3
b
2
b
1
b
0
Sign and
magnitude
1'
s complement
2'
s complement
B
V
alues represented
Figure 2.1. Binary, signed-integer representations.
Page 28

## Slide 26: Addition and Subtraction – 2’s Complement
4
+ 3
7
0100
0011
0111
-4
+ (-3)
-7
1100
1101
11001
4
- 3
1
0100
1101
10001
-4
+ 3
-1
1100
0011
1111
If carry-in to the high
order bit =
carry-out then ignore
carry
if carry-in differs from
carry-out then overflow
Simpler addition scheme makes twos complement the most common
choice for integer number systems within digital systems

## Slide 35: 2’s-Complement Add and Subtract Operations
1 1 0 1
0 1 1 1
0 1 0 0
0 0 1 0
1 1 0 0
1 1 1 0
0 1 1 0
1 1 0 1
0 0 1 1
1 0 0 1
0 1 0 1
1 1 1 0
1 0 0 1
1 1 1 1
1 0 0 0
0 0 1 0
0 0 1 1
0 1 0 1
4
+
(
)
2
-
(
)
3
+
(
)
2
-
(
)
8
-
(
)
5
+
(
)
+
+
+
+
+
+
1 1 1 0
0 1 0 0
1 0 1 0
0 1 1 1
1 1 0 1
0 1 0 0
6
-
(
)
2
-
(
)
4
+
(
)
3
-
(
)
4
+
(
)
7
+
(
)
+
+
(b)
(d)
1 0 1 1
1 1 1 0
1 0 0 1
1 1 0 1
1 0 0 1
0 0 1 0
0 1 0 0
0 1 1 0
0 0 1 1
1 0 0 1
1 0 1 1
1 0 0 1
0 0 0 1
0 0 1 0
1 1 0 1
0 1 0 1
0 0 1 0
0 0 1 1
5
-
(
)
2
+
(
)
3
+
(
)
5
+
(
)
2
+
(
)
4
+
(
)
2
-
(
)
7
-
(
)
3
-
(
)
7
-
(
)
6
+
(
)
3
+
(
)
1
+
(
)
7
-
(
)
5
-
(
)
7
-
(
)
2
+
(
)
3
-
(
)
+
+
-
-
-
-
-
-
(a)
(c)
(e)
(f)
(g)
(h)
(i)
(j)
Figure 2.4. 2's-complement Add and Subtract operations.
Page 31

## Slide 36: Overflow - Add two positive numbers to get a negative number or two negative numbers to get a positive number
5 + 3 = -8
-7 - 2 = +7
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1
0000
0001
0010
0011
1000
0101
0110
0100
1001
1010
1011
1100
1101
0111
1110
1111
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1

## Slide 37: Overflow Conditions
5
3
-8
0 1 1 1
0 1 0 1
0 0 1 1
1 0 0 0
-7
-2
7
1 0 0 0
1 0 0 1
1 1 0 0
1 0 1 1 1
5
2
7
0 0 0 0
0 1 0 1
0 0 1 0
0 1 1 1
-3
-5
-8
1 1 1 1
1 1 0 1
1 0 1 1
1 1 0 0 0
Overflow
Overflow
No overflow
No overflow
Overflow when carry-in to the high-order bit does not equal carry out

## Slide 38: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 39: Sign Extension Example
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;

## Slide 40: Memory Locations, Addresses, and Operations

## Slide 41: How do we Specify Memory Sizes

## Slide 42: How do we Specify Memory Sizes

## Slide 48: Examples
32-bit Integer 0x12345678:
  Big-Endian: 0x12 0x34 0x56 0x78
  Little-Endian: 0x78 0x56 0x34 0x12
32-bit Integer 0xAABBCCDD:
  Big-Endian: 0xAA 0xBB 0xCC 0xDD
  Little-Endian: 0xDD 0xCC 0xBB 0xAA
32-bit Integer 0xDEADBEEF:
  Big-Endian: 0xDE 0xAD 0xBE 0xEF
  Little-Endian: 0xEF 0xBE 0xAD 0xDE
32-bit Integer 0x80000000 (the minimum signed integer):
  Big-Endian: 0x80 0x00 0x00 0x00
  Little-Endian: 0x00 0x00 0x00 0x80
32-bit Integer 0xFFFFFFFF (all bits set to 1):
  Big-Endian: 0xFF 0xFF 0xFF 0xFF
  Little-Endian: 0xFF 0xFF 0xFF 0xFF

## Slide 49: Memory Location, Addresses, and Operation
Memory consists of many millions of storage cells, each of which can store 1 bit.
Data is usually accessed in n-bit groups. n is called word length.
second word
first word
Figure 2.5. Memory words.
n
bits
last word
i
th word
•
•
•
•
•
•

## Slide 50: Memory Location, Addresses, and Operation
32-bit word length example
(b) Four characters
character
character
character
character
(a) A signed integer
Sign bit:
for positive numbers
for negative numbers
ASCII
ASCII
ASCII
ASCII
32 bits
8 bits
8 bits
8 bits
8 bits
b
31
b
30
b
1
b
0
b
31
0
=
b
31
1
=
•
•
•

## Slide 51: Memory Location, Addresses, and Operation
To retrieve information from memory, either for one word or one byte (8-bit), addresses for each location are needed.
A k-bit address memory has 2k memory locations, namely 0 – 2k-1, called memory space.
24-bit memory: 224 = 16,777,216 = 16M (1M=220)
32-bit memory: 232 = 4G (1G=230)
1K(kilo)=210
1T(tera)=240

## Slide 52: Memory Location, Addresses, and Operation
It is impractical to assign distinct addresses to individual bit locations in the memory.
The most practical assignment is to have successive addresses refer to successive byte locations in the memory – byte-addressable memory.
Byte locations have addresses 0, 1, 2, … If word length is 32 bits, they successive words are located at addresses 0, 4, 8,…

## Slide 53: Big-Endian and Little-Endian Assignments
2
k
4
-
2
k
3
-
2
k
2
-
2
k
1
-
2
k
4
-
2
k
4
-
0
1
2
3
4
5
6
7
0
0
4
2
k
1
-
2
k
2
-
2
k
3
-
2
k
4
-
3
2
1
0
7
6
5
4
Byte address
Byte address
(a) Big-endian assignment
(b) Little-endian assignment
4
W
ord
address
•
•
•
•
•
•
Figure 2.7. Byte and word addressing.
Big-Endian: lower byte addresses are used for the most significant bytes of the word
Little-Endian: opposite ordering. lower byte addresses are used for the less significant bytes of the word

## Slide 54: Memory Location, Addresses, and Operation
Address ordering of bytes
Word alignment
  Words are said to be aligned in memory if they begin at a byte addr. that is a multiple of the num of bytes in a word.
    16-bit word: word addresses: 0, 2, 4,….
    32-bit word: word addresses: 0, 4, 8,….
    64-bit word: word addresses: 0, 8,16,….
Access numbers, characters, and character strings

## Slide 55: Memory Operation
Load (or Read or Fetch)
Copy the content. The memory content doesn’t change.
Address – Load
Registers can be used
Store (or Write)
Overwrite the content in memory
Address and Data – Store
Registers can be used

## Slide 56: Instruction and Instruction Sequencing

## Slide 57: “Must-Perform” Operations
Data transfers between the memory and the processor registers
Arithmetic and logic operations on data
Program sequencing and control
I/O transfers

## Slide 58: Register Transfer Notation
Identify a location by a symbolic name standing for its hardware binary address (LOC, R0,…)
Contents of a location are denoted by placing square brackets around the name of the location (R1←[LOC], R3 ←[R1]+[R2])
Register Transfer Notation (RTN)

## Slide 59: Assembly Language Notation
Represent machine instructions and programs.
Move LOC, R1 = R1←[LOC]
Add R1, R2, R3 = R3 ←[R1]+[R2]

## Slide 60: CPU Organization
Single Accumulator
  Result usually goes to the Accumulator
  Accumulator has to be saved to memory quite often
General Register
  Registers hold operands thus reduce memory traffic
  Register bookkeeping
Stack
  Operands and result are always in the stack

## Slide 61: Instruction Formats
Three-Address Instructions
  ADD R1, R2, R3 R1 ← R2 + R3
Two-Address Instructions
  ADD R1, R2 R1 ← R1 + R2
One-Address Instructions
  ADD M AC ← AC + M[AR]
Zero-Address Instructions
  ADD TOS ← TOS + (TOS – 1)
RISC Instructions
  Lots of registers. Memory is restricted to Load & Store
Instruction
Opcode
Operand(s) or Address(es)

## Slide 62: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Three-Address
  ADD R1, A, B ; R1 ← M[A] + M[B]
  ADD R2, C, D ; R2 ← M[C] + M[D]
  MUL X, R1, R2 ; M[X] ← R1  R2

## Slide 63: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Two-Address
  MOV R1, A ; R1 ← M[A]
  ADD R1, B ; R1 ← R1 + M[B]
  MOV R2, C ; R2 ← M[C]
  ADD R2, D ; R2 ← R2 + M[D]
  MUL R1, R2 ; R1 ← R1  R2
  MOV X, R1 ; M[X] ← R1

## Slide 64: Instruction Formats
Example: Evaluate (A+B)  (C+D)
One-Address
  LOAD A ; AC ← M[A]
  ADD B ; AC ← AC + M[B]
  STORE T ; M[T] ← AC
  LOAD C ; AC ← M[C]
  ADD D ; AC ← AC + M[D]
  MUL T ; AC ← AC  M[T]
  STORE X ; M[X] ← AC

## Slide 65: Instruction Formats
Example: Evaluate (A+B)  (C+D)
RISC
  LOAD R1, A ; R1 ← M[A]
  LOAD R2, B ; R2 ← M[B]
  LOAD R3, C ; R3 ← M[C]
  LOAD R4, D ; R4 ← M[D]
  ADD R1, R1, R2 ; R1 ← R1 + R2
  ADD R3, R3, R4 ; R3 ← R3 + R4
  MUL R1, R1, R3 ; R1 ← R1  R3
  STORE X, R1 ; M[X] ← R1

## Slide 66: Using Registers
Registers are faster
Shorter instructions
  The number of registers is smaller (e.g. 32 registers need 5 bits)
Potential speedup
Minimize the frequency with which data is moved back and forth between the memory and processor registers.

## Slide 67: Instruction Execution and Straight-Line Sequencing
R0,C
B,R0
A,R0
Move
i
+ 8
Begin execution here
Move
i
Contents
Address
C
B
A
the program
Data for
segment
program
3-instruction
Add
i
+ 4
Figure 2.8. A program for C ¬ [A] + [B].
Assumptions:
- One memory operand
per instruction
- 32-bit word length
- Memory is byte
addressable
- Full memory address
can be directly specified
in a single-word instruction
Two-phase procedure
Instruction fetch
Instruction execute
Page 43

## Slide 68: Branching
NUM
n
NUM2
NUM1
R0,SUM
NUM
n
,R0
NUM3,R0
NUM2,R0
NUM1,R0
Figure 2.9. A straight-line program for adding n numbers.
Add
Add
Move
SUM
i
Move
Add
i
4
n
+
i
4
n
4
-
+
i
8
+
i
4
+
•
•
•
•
•
•
•
•
•

## Slide 69: Branching
N,R1
Move
NUM
n
NUM2
NUM1
R0,SUM
R1
"Next" number to R0
Figure 2.10. Using a loop to add n numbers.
LOOP
Decrement
Move
LOOP
loop
Program
Determine address of
"Next" number and add
N
SUM
n
R0
Clear
Branch>0
•
•
•
•
•
•
Branch target
Conditional branch

## Slide 70: Condition Codes
Condition code flags
Condition code register / status register
N (negative)
Z (zero)
V (overflow)
C (carry)
Different instructions affect different flags

## Slide 71: Conditional Branch Instructions
Example:
  A: 1 1 1 1 0 0 0 0
  B: 0 0 0 1 0 1 0 0
A: 1 1 1 1 0 0 0 0
+(−B): 1 1 1 0 1 1 0 0
1 1 0 1 1 1 0 0
C = 1
S = 1
V = 0
Z = 0

## Slide 72: Status Bits
ALU
V
Z
S
C
Zero Check
Cn
Cn-1
Fn-1
A
B
F

## Slide 73: Addressing Modes

## Slide 74: Generating Memory Addresses
How to specify the address of branch target?
Can we give the memory operand address directly in a single Add instruction in the loop?
Use a register to hold the address of NUM1; then increment by 4 on each pass through the loop.

## Slide 75: Addressing Modes
Implied
  AC is implied in “ADD M[AR]” in “One-Address” instr.
  TOS is implied in “ADD” in “Zero-Address” instr.
Immediate
  The use of a constant in “MOV R1, 5”, i.e. R1 ← 5
Register
  Indicate which register holds the operand
Instruction
Opcode
Mode
...

## Slide 76: Addressing Modes
Register Indirect
  Indicate the register that holds the number of the register that holds the operand
    MOV R1, (R2)
Autoincrement / Autodecrement
  Access & update in 1 instr.
Direct Address
  Use the given address to access a memory location
R1
R2 = 3
R3 = 5

## Slide 78: Addressing Modes
Indirect Address
  Indicate the memory location that holds the address of the memory location that holds the data
AR = 101
100
101
102
103
104
Memory
0 1 0 4
1 1 0 A

## Slide 79: Addressing Modes
100
101
102
103
104
Memory
0
1
2
Relative Address
  EA = PC + Relative Addr
AR = 100
1 1 0 A
PC = 2
+
Program
Data
Could be Positive or Negative (2’s Complement)

## Slide 80: Addressing Modes
Indexed
  EA = Index Register + Relative Addr
100
101
102
103
104
Memory
AR = 100
1 1 0 A
XR = 2
+
Could be Positive or Negative (2’s Complement)
Useful with “Autoincrement” or “Autodecrement”

## Slide 82: Addressing Modes
Base Register
  EA = Base Register + Relative Addr
100
101
102
103
104
Memory
BR = 100
0 0 0 A
AR = 2
+
Could be Positive or Negative (2’s Complement)
Usually points to the beginning of an array
0 0 0 5
0 0 1 2
0 1 0 7
0 0 5 9

## Slide 83: Addressing Modes
The different ways in which the location of an operand is specified in an instruction are referred to as addressing modes.
Name
Assem
bler
syn
tax
Addressing
function
Immediate
#V
alue
Op
erand
=
V
alue
Register
R
i
EA
=
R
i
Absolute
(Direct)
LOC
EA
=
LOC
Indirect
(R
i
)
EA
=
[R
i
]
(LOC)
EA
=
[LOC]
Index
X(R
i
)
EA
=
[R
i
]
+
X
Base
with
index
(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
Base
with
index
X(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
+
X
and
offset
Relative
X(PC)
EA
=
[PC]
+
X
Autoincremen
t
(R
i
)+
EA
=
[R
i
]
;
Incremen
t
R
i
Autodecrement
(R
i
)
Decremen
t
R
i
;
EA
=
[R
i
]


## Slide 84: Indexing and Arrays
Index mode – the effective address of the operand is generated by adding a constant value to the contents of a register.
Index register
X(Ri): EA = X + [Ri]
The constant X may be given either as an explicit number or as a symbolic name representing a numerical value.
If X is shorter than a word, sign-extension is needed.

## Slide 85: Indexing and Arrays
In general, the Index mode facilitates access to an operand whose location is defined relative to a reference point within the data structure in which the operand appears.
Several variations: (Ri, Rj): EA = [Ri] + [Rj] X(Ri, Rj): EA = X + [Ri] + [Rj]

## Slide 86: Relative Addressing
Relative mode – the effective address is determined by the Index mode using the program counter in place of the general-purpose register.
X(PC) – note that X is a signed number
Branch>0 LOOP
This location is computed by specifying it as an offset from the current value of PC.
Branch target may be either before or after the branch instruction, the offset is given as a singed num.

## Slide 87: Additional Modes
Autoincrement mode – the effective address of the operand is the contents of a register specified in the instruction. After accessing the operand, the contents of this register are automatically incremented to point to the next item in a list.
(Ri)+. The increment is 1 for byte-sized operands, 2 for 16-bit operands, and 4 for 32-bit operands.
Autodecrement mode: -(Ri) – decrement first
R0
Clear
R0,SUM
R1
(R2)+,R0
Figure 2.16. The Autoincrement addressing mode used in the program of Figure 2.12.
Initialization
Move
LOOP
Add
Decrement
LOOP
#NUM1,R2
N,R1
Move
Move
Branch>0

## Slide 88: Data Transfer Instructions
Mode | Assembly | Register Transfer
Direct address | LD ADR | AC ← M[ADR]
Indirect address | LD @ADR | AC ← M[M[ADR]]
Relative address | LD $ADR | AC ← M[PC+ADR]
Immediate operand | LD #NBR | AC ← NBR
Index addressing | LD ADR(X) | AC ← M[ADR+XR]
Register | LD R1 | AC ← R1
Register indirect | LD (R1) | AC ← M[R1]
Autoincrement | LD (R1)+ | AC ← M[R1], R1 ← R1+1

## Slide 89: For(i=0;i<10;i++)C[i]=A[i]+B[i]
.data
A: .word 1, 2, 3, 4, 5 # Array A
B: .word 10, 20, 30, 40, 50 # Array B
C: .space 20 # Array C, reserved space for 5 integers
.text
.globl main
main:
li $t0, 5 # Mov #10, R1 # Number of elements (length of arrays)
la $t1, A # Mov #A, R2 # Load address of array A into $t1
la $t2, B # Mov #B, R3 # Load address of array B into $t2
la $t3, C # Mov #C, R5 # Load address of array C into $t3
li $t4, 0 # Mov #0, R6 # Initialize index register i = 0
Loop:
beq $t4, $t0, Exit # Branch if i == 5 (end of loop)
lw $t5, 0($t1) # Mov (R2), R4 # Load A[i] into $t5
lw $t6, 0($t2) # Mov (R3), R4 # Load B[i] into $t6
add $t7, $t5, $t6 # Add R4, (R3) # Add A[i] + B[i], store in $t7
sw $t7, 0($t3) # Mov R4, (R5) # Store the result in C[i]
addi $t1, $t1, 4 # Increment pointer for A[i]
addi $t2, $t2, 4 # Increment pointer for B[i]
addi $t3, $t3, 4 # Increment pointer for C[i]
addi $t4, $t4, 1 # Increment index i
j Loop # Jump back to Loop
Exit:
# Exit the program (for simulators)
li $v0, 10 # Exit system call
syscall

## Slide 90
Addressing Modes | Applications
Immediate Addressing Mode | To initialize registers to a constant value
Direct Addressing Mode and Register Direct Addressing Mode | To access static data To implement variables
Indirect Addressing Mode and Register Indirect Addressing Mode | To implement pointers because pointers are memory locations that store the address of another variable To pass array as a parameter because array name is the base address and pointer is needed to point the address
Relative Addressing Mode | For program relocation at run time i.e. for position independent code To change the normal sequence of execution of instructions For branch type instructions since it directly updates the program counter
Index Addressing Mode | For array implementation or array addressing For records implementation
Base Register Addressing Mode | For writing relocatable code i.e. for relocation of program in memory even at run time For handling recursive procedures
Auto-increment Addressing Mode and Auto-decrement Addressing Mode | For implementing loops For stepping through arrays in a loop For implementing a stack as push and pop

## Slide 93: Indexing and Arrays
Index mode – the effective address of the operand is generated by adding a constant value to the contents of a register.
Index register
X(Ri): EA = X + [Ri]
The constant X may be given either as an explicit number or as a symbolic name representing a numerical value.
If X is shorter than a word, sign-extension is needed.

## Slide 94: Indexing and Arrays
In general, the Index mode facilitates access to an operand whose location is defined relative to a reference point within the data structure in which the operand appears.
Several variations: (Ri, Rj): EA = [Ri] + [Rj] X(Ri, Rj): EA = X + [Ri] + [Rj]

## Slide 95: Relative Addressing
Relative mode – the effective address is determined by the Index mode using the program counter in place of the general-purpose register.
X(PC) – note that X is a signed number
Branch>0 LOOP
This location is computed by specifying it as an offset from the current value of PC.
Branch target may be either before or after the branch instruction, the offset is given as a singed num.

## Slide 96: Additional Modes
Autoincrement mode – the effective address of the operand is the contents of a register specified in the instruction. After accessing the operand, the contents of this register are automatically incremented to point to the next item in a list.
(Ri)+. The increment is 1 for byte-sized operands, 2 for 16-bit operands, and 4 for 32-bit operands.
Autodecrement mode: -(Ri) – decrement first
R0
Clear
R0,SUM
R1
(R2)+,R0
Figure 2.16. The Autoincrement addressing mode used in the program of Figure 2.12.
Initialization
Move
LOOP
Add
Decrement
LOOP
#NUM1,R2
N,R1
Move
Move
Branch>0

## Slide 97: Data Manipulation Instructions
Arithmetic
Logical & Bit Manipulation
Shift
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with carry | ADDC
Subtract with borrow | SUBB
Negate | NEG
Name | Mnemonic
Clear | CLR
Complement | COM
AND | AND
OR | OR
Exclusive-OR | XOR
Clear carry | CLRC
Set carry | SETC
Complement carry | COMC
Enable interrupt | EI
Disable interrupt | DI
Name | Mnemonic
Logical shift right | SHR
Logical shift left | SHL
Arithmetic shift right | SHRA
Arithmetic shift left | SHLA
Rotate right | ROR
Rotate left | ROL
Rotate right through carry | RORC
Rotate left through carry | ROLC

## Slide 98: Program Control Instructions
Name | Mnemonic
Branch | BR
Jump | JMP
Skip | SKP
Call | CALL
Return | RET
Compare (Subtract) | CMP
Test (AND) | TST
Subtract A – B but don’t store the result
1
0
1
1
0
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
Mask

## Slide 99: Conditional Branch Instructions
Mnemonic | Branch Condition | Tested Condition
BZ | Branch if zero | Z = 1
BNZ | Branch if not zero | Z = 0
BC | Branch if carry | C = 1
BNC | Branch if no carry | C = 0
BP | Branch if plus | S = 0
BM | Branch if minus | S = 1
BV | Branch if overflow | V = 1
BNV | Branch if no overflow | V = 0

## Slide 100: Additional Instructions

## Slide 101: Logical Shifts
Logical shift – shifting left (LShiftL) and shifting right (LShiftR)
C
R0
0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
0
0
1
1
1
0
0
0
(b) Logical shift r
ight
LShiftR #2,R0
(a) Logical shift left
LShiftL #2,R0
C
R0
0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
1
0
.
.
.
0
0
1
0
1
.
.
.

## Slide 102: Arithmetic Shifts
C
before:
after:
0
1
1
1
0
0
0
1
.
.
.
0
1
1
1
0
0
1
0
1
1
(c) Ar
ithmetic shift r
ight
AShiftR #2,R0
R0
.
.
.

## Slide 103: Rotate
Figure 2.32. Rotate instructions.
C
R0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
0
1
1
1
0
0
1
(c) Rotate r
ight without carr
y
RotateR #2,R0
(a) Rotate left without carr
y
RotateL #2,R0
C
R0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
1
0
.
.
.
1
0
1
0
1
C
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
0
1
1
1
0
0
0
(d) Rotate r
ight with carr
y
RotateRC #2,R0
R0
.
.
.
.
.
.
(b) Rotate left with carr
y
RotateLC #2,R0
C
R0
before:
after:
0
1
0
0
0
1
1
1
.
.
.
1
1
1
1
0
.
.
.
0
0
1
0
1

## Slide 104: Multiplication and Division
Not very popular (especially division)
Multiply Ri, Rj Rj ← [Ri] х [Rj]
2n-bit product case: high-order half in R(j+1)
Divide Ri, Rj Rj ← [Ri] / [Rj]
  Quotient is in Rj, remainder may be placed in R(j+1)

## Slide 105: Encoding of Machine Instructions

## Slide 106: Encoding of Machine Instructions
Assembly language program needs to be converted into machine instructions. (ADD = 0100 in ARM instruction set)
In the previous section, an assumption was made that all instructions are one word in length.
OP code: the type of operation to be performed and the type of operands used may be specified using an encoded binary pattern
Suppose 32-bit word length, 8-bit OP code (how many instructions can we have?), 16 registers in total (how many bits?), 3-bit addressing mode indicator.
Add R1, R2
Move 24(R0), R5
LshiftR #2, R0
Move #$3A, R1
Branch>0 LOOP
OP code
Source
Dest
Other info
8
7
7
10
(a) One-word instruction

## Slide 107: Encoding of Machine Instructions
What happens if we want to specify a memory operand using the Absolute addressing mode?
Move R2, LOC
14-bit for LOC – insufficient
Solution – use two words
(b) Two-word instruction
Memory address/Immediate operand
OP code
Source
Dest
Other info

## Slide 108: Encoding of Machine Instructions
Then what if an instruction in which two operands can be specified using the Absolute addressing mode?
Move LOC1, LOC2
Solution – use two additional words
This approach results in instructions of variable length. Complex instructions can be implemented, closely resembling operations in high-level programming languages – Complex Instruction Set Computer (CISC)

## Slide 109: Encoding of Machine Instructions
If we insist that all instructions must fit into a single 32-bit word, it is not possible to provide a 32-bit address or a 32-bit immediate operand within the instruction.
It is still possible to define a highly functional instruction set, which makes extensive use of the processor registers.
Add R1, R2 ----- yes
Add LOC, R2 ----- no
Add (R3), R2 ----- yes